Photon statistics of a superradiant laser based on cold atoms of Strontium-88
Neven Gentil
supervised by
Stefan A.Schäffer
1

---
Summary:
What is superradiance? How do we achieve this state of lasing?
The superradiant experiment: atoms of strontium and the multilevel structure
The first order correlation function g¹: what does this physically mean?
Standard setup for g¹ and its limitations
The balanced heterodyne setup
Electronic noise reduction
Power to noise ratio and other verifications
g¹ for a standard laser
g¹ for the superradiant laser
Numerical simulation as a comparison: master equation & cumulants expansion method
Conclusion.
Introduction
Experiment
Results
2

---
Cavity: two partially reflective mirrors. One mode of the cavity must fit the gain medium frequency: they must be in “resonance”
Composition of a laser: cavity + gain medium
𝜿: cavity loss rate
By constructive/destructive interference, the cavity field is restricted to well defined frequencies (called “modes”)
Gain medium: any “two-level” system
Excited state
g
Two possibilities:
g ≫ 𝜿: strong coupling
g ≪ 𝜿: weak coupling
Cavity modes
“Rest” state
g: coefficient describing the strength of interaction between the gain medium and the cavity field/modes
What is superradiance? How do we achieve this state of lasing? - 3

---
The cavity loss rate (𝜿) is linked to the reflectivity of the mirrors (coefficient “r”)
High reflectivity: narrow linewidth for the cavity modes = narrow cavity linewidth
Low reflectivity: broad linewidth for the cavity modes = broad cavity linewidth
What is superradiance? How do we achieve this state of lasing? - 3
Transmission

---
“Standard” laser = good cavity regime ⟹ the gain linewidth is broader than the cavity linewidth
This is achieved by high reflectivity of the mirrors: the photons inside the cavity need many round-trip before exiting.
gain linewidth
cavity linewidth
𝜔
The output frequency spectrum is restricted to the narrower linewidth: here the cavity linewidth.
The cavity linewidth is influenced by mechanical fluctuations ⟹ the spectrum linewidth is influenced by mechanical fluctuations
What is superradiance? How do we achieve this state of lasing? - 3

---
“Superradiant” laser = bad cavity regime ⟹ the gain linewidth is narrower than the cavity linewidth
This is achieved by low reflectivity of the mirrors: the photons quickly exit the cavity
gain linewidth
cavity linewidth
𝜔
The output frequency spectrum is restricted to the gain linewidth.
Thanks to the few round-trip, the gain linewidth is almost not influenced by mechanical fluctuations ⟹ the frequency spectrum is mainly determined by the two-level transition spectrum of the gain medium.
What is superradiance? How do we achieve this state of lasing? - 3

---
Superradiance:
Bad-cavity regime
Strong-collective coupling
Coherence time/length determined by the gain medium, here cold atoms of Strontium-88. In theory, the output linewidth may be as narrow as the transition linewidth used.
The cavity is weakly coupled to one single atom (g ≪ 𝜿) but the strongly coupled to the ensemble (Ng ≫ 𝜿 with N the number of atoms)
What is superradiance? How do we achieve this state of lasing? - 3

---
Why 88Sr?
The most abundant isotope of strontium at ∼82% by mass.
No nuclear spin: simpler level structure compared to other isotopes and makes it easier to work with, especially for the many transitions involved in the repumping/cooling scheme.
Two electrons in their outermost shell: structure of electronic transitions that is particularly useful in quantum metrology.
The transition 1S0 -3P1 has a linewidth of 7.5 kHz.
The superradiant experiment: atoms of strontium and the multilevel structure - 4

---
Non-stationary case
Stationary case
“You shall
not pass!”
Frontier of the
quantum world
Non-stationary case
Stationary case
The first order correlation function g¹: what does this physically mean? - 4

---
Perfectly coherent signal (perfectly well defined phase and frequency)
Chaotic signal generated by collision broadening (random phase jumps)
Perfectly coherent light
“Gaussian” light
“Lorentzian” light
The first order correlation function g¹: what does this physically mean? - 4

---
Standard setup for g¹ and its limitations - 4

---
Limitations?
Standard setup for g¹ and its limitations - 4

---
Remove correlated noise
Power tuned by local oscillator
Frequency difference
The balanced heterodyne setup - 4

---
Electronic noise reduction - 4

---
Electronic noise reduction - 4

---
Power to noise ratio and other verifications - 4

---
Power to noise ratio and other verifications - 4

---
Power to noise ratio and other verifications - 4

---
Power to noise ratio and other verifications - 4

---
Power to noise ratio and other verifications - 4

---
g¹ for a standard laser - 4

---
g¹ for a standard laser - 4

---
g¹ for a standard laser - 4

---
g¹ for the superradiant laser - 4

---
g¹ for the superradiant laser - 4

---
g¹ for the superradiant laser - 4

---
Numerical simulation as a comparison: master equation & cumulants expansion method - 4

---
Numerical simulation as a comparison: master equation & cumulants expansion method - 4

---
Conclusion
4